| Assessor Name: M White CMIOSH DipSM | Location: | Date: 06 02 2010 |
| --- | --- | --- |
| Equipment being assessed: Airvend Security Bag Vending Machine | Review Date: N/A | Copied to: Andy Taylor |

Airvend Uk Ltd                                PUWER 1998              Risk assessment

| Risk Matrix | Control Measures | Instructions for Completion |
| --- | --- | --- |
|  | (Risk Assessment, Method Statement, Permit to Work, Sequencing) |  |
|  | 15-25: Very high risks with potential of serious consequences. Eliminate risk by review of options and change as a priority. 8-12: Reduce risks identified to as low as reasonably practicable by specific controls, planning and supervision. Provision of special method statements and instruction of all parties involved. 3-6: Acceptable providing risks are managed and activities are carried out by competent personnel in accordance with safe working practices and statutory obligations. 1-2: No further consideration required. | A risk is the likelihood of a substance, activity or process to cause harm. Risk is also linked to the severity of its consequences and can be reduced. L = Likelihood S = Severity RR = Risk Rating (i.e. LxS) |

| Description of equipment | Persons Affected | Associated Risks | Risk Evaluation | Control Measures | Residual Risk | Responsibility for implementation | Responsibility for monitoring |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | L | S | RR |  | L | S | RR |  |  |
| The Airvend security bag vending machine is of heavy duty metal welded construction with a high impact shatter proof lexan globe which holds 48mm capsules containing four re-sealable plastic bags. It is 48” high, 16” wide and 16” deep. The machines will be maintained by Airvend personnel. | Members of the public Airport staff | Fire Machine being knocked over Resulting in bodily injury | 3 3 | 4 3 | 12 9 | There are no heat sources or other sources of ignition within the equipment and is deemed to comply with BS 476 Part 6 – Fire Propagation (Class 0) However, it should be noted that the globe and capsules may support combustion in a general fire situation. The machine has a substantial base which would prevent the machine being knocked over in normal use. However, with some effort the machine could be knocked over causing injury to a person. It is recommended that the machine be positioned in a location where it is not likely to be knocked over. Otherwise the machine should be secured to a wall or its base secured to the floor. | 1 1 | 4 3 | 4 3 | AT AT | AT AT |